## Slide 1
A development of Compact Triple band Receiver for millimeter-wave radio astronomy
Korea Astronomy and Space Science Institute (KASI)
Seog-Tae Han and KVN receiver group
sthan@kasi.re.kr
8-11 October 2018, Granada, Spain

## Slide 2: Motivation and Overview
The middle of April 2015 : Drs. Richard Dodson and Maria Rioja
* Why don’t you make “Compact Triple band receiver(CTR)” to be installed any radio telescope, Not like that of KVN
Oct. 5~7 2015 : ERA Tec workshop, Florence, Italy
* Proposed “ Conceptual design of CTR”
Sept. 20 , 2016 : 2016 EVN symposium, St. Petersburg, Russia
* Presented “ Development of Quasi-optical circuit for CTR”
Today(after 3 and half years) : 2018 EVN symposium, Granada, Spain
* Present “ Development and test observations results of CTR”
Conceptual design of CTR

## Slide 3: Development of CTR
K-band : 18~26GHz
Observing bandwidths
Q-band : 35~50GHz
W-band : 85~116GHz
IF bandwidths
Given next page
Receiver noise temperature
Polarization
RHCP
LHCP
8~16GHz
W-band horn
K-band horn
Q-band
horn
HPF
LPF
Mirror
Mirror
380 mm
600 mm x 600 mm
370 mm
Beams from antenna
Operation Mode
SSB

## Slide 4: Measured receiver noise temperatures
Goal of receiver noise temperature
- K-band : < 20 K, - Q-band : < 30K, W-band : < 60 K
Focusing on development of critical components to improve the noise temperatures
- OMT (Ortho-mode Transducer), Phase shifter (Polarizer), Coupler, Cryogenic LNAs
K-band
Q-band
W-band
8 ~ 16 GHz

## Slide 5: W-band Receiver Block diagram of CTR
The critical components in terms of noise temperature have been developing at KASI
- OMT (Ortho-mode Transducer), Phase shifter (Polarizer) and Coupler
Used LNF cryogenic low noise amplifiers for K-, Q-, and W-band
- LNF( Low Noise Factory), Sweden
RHCP
LHCP

## Slide 6: 1. Beam Alignment
Used Venus at EL = 28 degree and with 86 GHz pointing model
Pointing offsets among 3 channels : less than 3 arcsec ( ~ 1/10 of HPBW of 100 GHz)
Test observations
2. Antenna Beam Patterns(1)
K-band
Mars (size = 20 arcsec) @ EL = 26
Contour = -1dB step from Peak
OTF observation method
Q-band
W-band

## Slide 7
2. Antenna Beam Patterns and HPBW(2)
Frequency (GHz) | Measured (arcsec) | (arcsec)
105 | 28 | 28
44 | 66 | 67
23 | 123 | 128
𝛌/D
𝛌/D
HPBWs of KVN Antenna
High side-lobe levels such 12 dB more than that of general cassegrain antenna as expected due to shaped cassegrain antenna
Symmetric beam patterns
- Good agreement with theoretical and measured values.
- Well designed quasi-optical circuit

## Slide 8: 3. Aperture Efficiency (1)
Mars @ EL = 25 – 28 degree
Mars brightness Temperature (30 - 115GHz)
  http://www.lesia.obspm.fr/perso/emmanuel-lellouch/mars/
K-band | Freq (GHz) | 18.5 | 21 | 23 | 25
 | A. E.(%) | 69 | 67 | 70 | 65
Q-band | Freq (GHz) | 35.5 | 40 | 44 | 49
 | A. E. (%) | 64 | 66 | 68 | 73
W-band | Freq (GHz) | 85.5 | 95 | 105 | 110
 | A. E. (%) | 61 (53) | 49 | 47 | 44
We obtained maximum aperture efficiency given KVN antenna properties
- Well designed quasi-optical circuit of CTR
61% at 85.5 GHz is due to mixed image signal

## Slide 9: Comparison with KVN 4 channel receivers. (2)
total surface error in mm
@ EL = 27
We obtained maximum aperture efficiency given KVN antenna properties
- Total surface rms with 145 micrometer of KVN antenna

## Slide 10: Simultaneous observation results(1)
19.97 GHz
36.17 GHz
115.27 GHz
22.23 GHz
86.24GHz
43.12 GHz

## Slide 11: Simultaneous observation result (2)
22.23 GHz
115.27GHz
43.12 GHz
22.23 GHz
110.20GHz
43.12 GHz

## Slide 12
Summary
Current KVN receiver optics
2300 mm
2600 mm
Pointing offset among 3 channels : less than 3 arcsec to conduct simultaneous observations
600 x 980 x 370 mm
Aperture efficiencies : Obtained as much as we could (K- : 68 %, Q-: 66 %, W-band : 50%)
CTR is tailorable for use in telescopes with a small receiver cabin.
Receiver noise temperatures : Not bad, but have to be improved (OMT, Polarizer and LNA)
Ultimately this concept may lead to development of much more compact multi-frequency receiver systems for mm-wave and sub-mm radio telescopes

## Slide 13
Not only I am very much proud of my colleagues
and their achievements,
But also I would like to really appreciate for their efforts
and passions for KVN
Thanks for your attention